## Slide 1
Alternate Views
© 2012 Project Lead The Way, Inc.
Introduction to Engineering Design

## Slide 2: Alternate Views
In some cases, orthogonal projections and pictorials are not sufficient to specify all the details of a part.
  Section View. Used to show “inside” details not apparent on the exterior of the part
  Auxiliary View. Used to show features that are located on an inclined surface in true size and shape
  Detail View. Used to show a “close-up” view of features that are too small to adequately specify in another view

## Slide 3: Section View
Provides a view of an object as if it were cut by a saw
Location is indicated by a cutting plane line on another view
Cutting plane line

## Slide 4: Section View
Cutting plane line
  Indicates location of the cut
  Thick and broken line
  Arrows indicate direction of view
  Labeled with a letter for identification on drawing
Cutting plane line

## Slide 5: Section View
Section lines
  Hatch lines that indicate material that was “cut” at the cutting plane line
  Thin lines
Cutting plane line
Section lines

## Slide 6: Section View
Types
  Full Section
  Half Section
  Offset Section

## Slide 7: Full Section
Cutting plane line passes fully through the part
The part of the object behind the cutting plane line (away from the direction of the arrows) is removed

## Slide 8: Full Section Example
This half of the part is removed
Section lines indicate material that is cut by the cutting plane line
Imagine the part is cut at cutting plane line
Direction of View

## Slide 9: Full Section Example
This half of the part is removed
Section lines indicate material that is cut by the cutting plane line
Imagine the part is cut at cutting plane line
Direction of View

## Slide 10: Half Section
Used on symmetrical parts to show inside as well as outside details in one view
One quarter of the part is cut away
Cutting plane line goes halfway through the part

## Slide 11: Half Section Example
Half Section
Note that the cutting plane line cuts away a quarter of the part
Only one arrowhead in the direction of view

## Slide 12: Offset Section
Interior features not in line with each other can be shown in an offset section view
Note how the cutting plane line changes direction and follows the center of each feature

## Slide 13: Auxiliary Views
Orthographic projection of an inclined plane (angled surface) which appears foreshortened in a principle orthographic projection
Used to show the true size and shape of an inclined plane and the features on it

## Slide 14: Auxiliary Views
Foreshortened surfaces do not give a clear or accurate representation of the size or shape of the surface or features and should not be dimensioned
foreshortened face
TOP
FRONT
RIGHT SIDE

## Slide 15: Auxiliary Views
An auxiliary view allows the viewer to look perpendicular to an angled surface to witness the true size and shape of that surface and its features (a hole in this example).
TOP
FRONT
RIGHT SIDE
True Height
Auxiliary Distance
Notes: We will not use auxiliary views in this unit, but they will be presented in more detail in Unit 8.

## Slide 16: Detail Views
An enlargement of a portion of another view to illustrate small features on a part
  Not to be confused with a Detail Drawing which is any drawing that contains all the information needed to manufacture a part

## Slide 17: Detail View Example
A feature is broken out and enlarged for clarity