## Slide 1
Holes and Hole Notes
© 2012 Project Lead The Way, Inc.
Introduction to Engineering Design

## Slide 2: Hole Definitions
Through/Thru
  Hole cuts through entire thickness
Clearance
  Hole large enough to allow screw head (and driver) to pass through
Blind
  Hole does not cut through entire thickness

## Slide 3: Hole Definitions
Countersink
  Conical-shaped recess around hole at surface
  Often used to accept tapered screw
Counterbore
  Cylindrical recess around hole at surface
  Often used to receive a bolt head or nut
Tapped
  Hole has internal threads

## Slide 4: Hole Note Symbols

## Slide 5: Hole Notes
A 0.25” diameter blind hole is drilled 0.75” deep. Then a 0.38” diameter counter bore is drilled 0.25” deep.
Counterbore or Spotface symbol
Depth
symbol

## Slide 6: Hole Notes
A 0.38” diameter blind hole is drilled 0.50” deep.

## Slide 7: Hole Notes
A 0.38” diameter hole is drilled completely through the object.

## Slide 8: Hole Notes
A 0.50” diameter hole is drilled completely through the object. Then a countersink is created with a 1.00” diameter at the surface and tapering at 82º.
Countersink or symbol

## Slide 9: Thread Notes
Thread are dimensioned with the use of local notes.
Two methods
  Unified National Thread method
  ISO

## Slide 10: Unified National Thread Notes
Thread per Inch
Major Diameter
Coarse or Fine threads. In this case C for course, F is for fine.

## Slide 11: ISO Thread Notes
M for Metric
12, Nominal Diameter in mm
1.5, Pitch of the threads
6, Grade of tolerance in the threads. Can be whole number from 3 to 9.
H, allowance. H means no allowance, G means tight allowance.
Prior to THRU may appear an LH for Left Hand thread